## Slide 1
2017
Pulse powder fire extinguishing systems SAPFIRE
Sapfir s.r.o.

## Slide 2
CE Certificate

## Slide 3
Certificate of Compliance

## Slide 4
Why choose MPH “TUNGUS”?
High reliability and efficiency
Relatively low price
12 years of operation without the necessary maintenance
Easy installation and operation
Blocking the fire at an early stage in the self-triggering or automatic modes
Versatility – can extinguish fires of all classes, including electrical units under voltage
Ability to extinguish by both: Volume and Surface
Minimal damage in case of fire in buildings in comparison to water extinguishing
Cheap maintenance

## Slide 5
1 - Trunk of a module
2 – Fire extinguishing powder
3 - Cold gas generator
4 - Electric activator
5 - Dispenser
6 - Membrane
Construction of a module
3
1
2
4
5
6

## Slide 6
1 - Trunk of a module
2 – Fire extinguishing powder
3 - Cold gas generator
4 - Dispenser
5 - Membrane
6 - Electrical box
8 - Electrical input
9 - Mount cover
10 - Console
Construction of a module
1
2
3
4
5
11
6
8
9
7
10

## Slide 7
MPH - 0.65
Name of a parameter |  | Value
The volume of housing, liter |  | 0.49
Total weight, kg |  | 3.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 0.49
Size, mm | height | 130
 | length | 230
Protected surface (S), m2 | Class А | 1.2
 | Class B | 1.2
Protected volume, m3 | Class А | 2.4
 | Class B | 1.2
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment
Technical parameters

## Slide 8
MPH - 2
Name of a parameter |  | Value
The volume of housing, liter |  | 2.2
Total weight, kg |  | 5.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 1.9
Size, mm | diameter | 124
 | length | 280
Protected surface, m2 | Class А | 15
 | Class B | 13
Protected volume, m3 | Class А | 28
 | Class B | 18
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 15 m2 and volume up to 28 m3.
Technical parameters

## Slide 9
MPH – 2.8
Name of a parameter |  | Value
Objem krytu, liter |  | 2.8
Total weight, kg |  | 5.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 4.8
Size, mm | diameter | 155
 | length | 215
Protected surface, m2 | Class А | 32
 | Class B | 14
Protected volume, m3 | Class А | 65
 | Class B | 17
Activation current, A |  | 0.12
Service life, years |  | 12
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
Technical parameters
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 32 m2 and volume up to 65 m3.

## Slide 10
MPH - 4
Name of a parameter |  | Value
The volume of housing, liter |  | 4.3
Total weight, kg |  | 7.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 4.0
Size, mm | diameter | 280
 | length | 195
Protected surface, m2 | Class А | 40
 | Class B | 16
Protected volume, m3 | Class А | 100
 | Class B | 20
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 40 m2 and volume up to 100 m3
Technical parameters

## Slide 11
MPH - 4
Name of a parameter |  | Value
The volume of housing, liter |  | 4.3
Total weight, kg |  | 7.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 4.0
Size, mm | diameter | 280
 | length | 195
Protected surface, m2 | Class А | 40
 | Class B | 16
Protected volume, m3 | Class А | 100
 | Class B | 20
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 40 m2 and volume up to 100 m3
Technical parameters

## Slide 12
MPH – 5
Name of a parameter |  | Value
The volume of housing, liter |  | 4.4
Total weight, kg |  | 8.2
Weight of the fire extinguishing powder ISTO-1, kg |  | 4.4
Size, mm | diameter | 280
 | length | 210
Protected surface, m2 | Class А | 78
 | Class B | -
Protected volume, m3 | Class А | 100
 | Class B | 40
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 78 m2 and volume up to 100 m3
Application Area:
Raised floors and suspended ceilings, attic and basement
Technical parameters

## Slide 13
MPH – 5M
Name of a parameter |  |  | Value
The volume of housing, litre |  |  | 4.7
Total weight, kg |  |  | 8.2
Weight of the fire extinguishing powder ISTO-1, kg |  |  | 4.4
Size, mm | diameter |  | 300
 | length |  | 280
Protected surface, m2 | Class А |  | 200
 | Class B |  | 78
Protected volume, m3 | Class А |  | 100
 | Class B |  | 40
Activation current, A |  |  | 0.12
Service life, years |  |  | 10
Anti explosion label |  | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
Module meant to be thrown into the fire, with manual start
Technical parameters

## Slide 14
MPH - 6
Name of a parameter |  | Value
The volume of housing, liter |  | 6.5
Total weight, kg |  | 10.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 6.0
Size, mm | diameter | 286
 | length | 233
Protected surface, m2 | Class А | 50
 | Class B | 27
Protected volume, m3 | Class А | 150
 | Class B | 38
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 50 m2 and volume up to150 m3
Technical parameters

## Slide 15
MPH - 9
Name of a parameter |  | Value
The volume of housing, liter |  | 9.0
Total weight, kg |  | 13.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 8.6
Size, mm | diameter | 286
 | length | 268
Protected surface (S), m2 | Class А | 72
 | Class B | 33
Protected volume, m3 | Class А | 216
 | Class B | 42
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 72 m2 and volume up to 216 m3
Technical parameters

## Slide 16
MPH - 9
Name of a parameter |  | Value
The volume of housing, liter |  | 9.0
Total weight, kg |  | 13.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 8.6
Size, mm | diameter | 286
 | length | 268
Protected surface (S), m2 | Class А | 72
 | Class B | 33
Protected volume, m3 | Class А | 216
 | Class B | 42
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
Technical parameters
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 72 m2 and volume up to 216 m3

## Slide 17
MPH – 10st
Name of a parameter |  | Value
The volume of housing, liter |  | 9.5
Total weight, kg |  | 20.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 9.5
Size, mm | diameter | 397
 | length | 305
Protected surface , m2 | Class А | 310
 | Class B | 80
Protected volume, m3 | Class А | 36
 | Class B | 240
Activation current, A |  | 0.12
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
Technical parameters
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 80 m2 and volume up to 240 m3

## Slide 18
MPH - 24
Name of a parameter |  | Value
The volume of housing, liter |  | 24.0
Total weight, kg |  | 36.0
Weight of the fire extinguishing powder ISTO-1, kg |  | 22.0
Size, mm | diameter | 245
 | length | 694
Protected surface , m2 | Class А | 75
 | Class B | 58
Protected volume, m3 | Class А | 250
 | Class B | -
Activation current, A |  | 0.2
Service life, years |  | 10
Anti explosion label | 0ЕхiaIIВT3 Х, RP ЕхiaI Х | 
The module is designed to extinguish hotbeds of ignition in closed cabinets with electronic and electrical equipment of small volume, cable channels, technological equipment on the surface up to 75 m2 and volume up to 250 m3
Technical parameters

## Slide 19: Device of the autonomous activation TPS – 01 Thermal fire-fighting sensor
Purpose:
Autonomous launch of up to 6 MPH modules in case of fire
Modifications:
TPS – 01-72
TPS – 01-93
TPS – 01-110
TPS – 01-М
Made in Slovakia

## Slide 20: TPS – 01-72 Thermal fire-fighting sensor
Name |  | Value
Weight, g |  | ≤ 200
Size | Diameter, mm | 65,0
 | Length, mm | 85,0
Operational temperature range, C |  | -60 ÷ +55
Temperature of automatic activation, C |  | +72 ± 5
Impulse, generated by 1 Ohm resistance | Amplitude, V | 3.5
 | Amplitude, A | 3.0
 | Length, ms | 1
Anti explosion label |  | 1ExibIIBT4
Service span without maintenance |  | 10
Purpose: TPS is unique autonomous Thermal activation and detection device that allows you to capture fire and activate powder, aerosol or gas fire suppression system.
Made in Slovakia

## Slide 21: TPS – 01-93 Thermal fire-fighting sensor
Name |  | Value
Weight, g |  | ≤ 200
Size | Diameter, mm | 65,0
 | Length, mm | 85,0
Operational temperature range, C |  | -60 ÷ +70
Temperature of automatic activation, C |  | +93 ± 5
Impulse, generated by 1 Ohm resistance | Amplitude, V | 3.5
 | Amplitude, A | 3.0
 | Length, ms | 1
Anti explosion label |  | 1ExibIIBT4
Service span without maintenance |  | 10
Purpose: TPS is unique autonomous Thermal activation and detection device that allows you to capture fire and activate powder, aerosol or gas fire suppression system.
Made in Slovakia

## Slide 22: TPS – 01-110 Thermal fire-fighting sensor
Name |  | Value
Weight, g |  | ≤ 200
Size | Diameter, mm | 65,0
 | Length, mm | 85,0
Operational temperature range, C |  | -60 ÷ +100
Temperature of automatic activation, C |  | +110 ± 5
Impulse, generated by 1 Ohm resistance | Amplitude, V | 3.5
 | Amplitude, A | 3.0
 | Length, ms | 1
Anti explosion label |  | 1ExibIIBT4
Service span without maintenance |  | 10
Purpose: TPS is unique autonomous Thermal activation and detection device that allows you to capture fire and activate powder, aerosol or gas fire suppression system.
Made in Slovakia

## Slide 23: TPS – 01-110 Manual trigger
Name |  | Value
Weight, g |  | ≤ 200
Size | Diameter, mm | 65,0
 | Length, mm | 85,0
Operational temperature range, C |  | -60 ÷ +100
Temperature of activation, C |  | manual
Impulse, generated by 1 Ohm resistance | Amplitude, V | 3.5
 | Amplitude, A | 3.0
 | Length, ms | 1
Antiexplosion label |  | 1ExibIIBT4
Service span without maintenance |  | 12
Purpose: TPS is unique autonomous manual activation device that allows capture of fires and manual activation of powder, aerosol or gas fire suppression system.
Made in Slovakia

## Slide 24
Made in Slovakia
Modifications:
TPS – 01C-72
TPS – 01C-93
TPS – 01C-110
Name |  | Value
Weight, g |  | ≤ 200
Size | Diameter, mm | 65,0
 | Length, mm | 85,0
Operational temperature range, C |  | -60 ÷ +100
Impulse, generated by 1 Ohm resistance | Amplitude, V | 3.5
 | Amplitude, A | 3.0
 | Length, ms | 1
Antiexplosion label |  | 1ExibIIBT4
Service span without maintenance |  | 12
Purpose: TPS is unique autonomous Thermal activation and detection device that allows capture of fire and activation of powder, aerosol or gas fire suppression systems. The apparatus also includes the possibility of a signal delivery to the fire panel and a switch for electronic equipment or activation of the alarm system.

## Slide 25
Autonomous activation device TPS – 01

## Slide 26: SA-01.1 Alarm system
Made in Slovakia

## Slide 27
SA-01
The alarm siren with beacon
Technical parameters SA-01
Sizes of the siren, mm 76×79×204
Sizes of the box, mm 245×190×100
Weight, kg 1,150
Voltage, V 230,0
Power, W 6,0
Sound volume, dB 92,0
Electricity consumption, A 0,1
Color of lamp cover Oranžová (červena)
Type of the acoustic signal Alarm
Level of coverage (IP) IP43
Activation device TPS-01
Range of operational temperature, °C -30 ÷ +50
Made in Slovakia

## Slide 28
Name of the parameter | Value
Number of modules in a single system | 2
Protected surface, m2 | 150
Protected volume, m3 | 500
Operational temperature range, °C: | -50 ÷ +50
Service span, years | 12
Fire extinguishing casette TPS-2.24
Made in Slovakia
Usage:
Usage of the casette as a part of the fire protection vehicle, visibly rases the abilities of the fire extinguishing squad and lowers the chance of burns and various dangers when extinguishing fires on the heigth. It also allows to easily block the hotbeds and protect the personell in the rooms where fire has already spread.
Casette TPS-2.24 is built from two modules of powder fire extinguishing MPH MPH-24 and is a device of the multiple usage. It also does not require any technical maintenance for 12 years of service.

## Slide 29
Name | Hodnota
The number of modules in the system, pieces | 4
Protected surface, m2 | 300
Protected volume, m3 | 1000
Operational temperature, °C | -50 ÷ +50
Span of service without maintenance, years | 12
Mobile fire fighting system TPS -4.24

## Slide 30
Mobile fire fighting system TPS-12.24
Made in Slovakia
Name |  | Value
Weight (without carrier), kg |  | ≤ 630
Size, mm | Height | 1400,0
 | Length | 2000,0
 | Width | 1500,0
Protected surface, m2 | Class A | 900
 | Class B | 700
Protected volume, m3 | Class A | 6000
 | Class B | -
Activation method |  | Manual
Operational temperature, C |  | -50 ÷ +50
Span of service without maintenance, years |  | 12

## Slide 31
Antifire system SA10.001.01. 2015
CRH (Slovensko) a.s.

## Slide 32
Antifire system SA10.001.01. 2015
Made in Slovakia

## Slide 33
Antifire system SA10.001.01. 2015
Made in Slovakia

## Slide 34
Antifire system SA10.001.01. 2015
CRH (Slovensko) a.s.
Made in Slovakia

## Slide 35
Antifire System SA10.005.01.2016
CRH (Slovensko) a.s.

## Slide 36
Antifire System SA10.005.01.2016
CRH (Slovensko) a.s.
Made in Slovakia

## Slide 37
Antifire System SA10.005.01.2016
CRH (Slovensko) a.s.
Made in Slovakia

## Slide 38
Antifire System SA10.011.01.2016
CRH (Slovensko) a.s.

## Slide 39
Antifire System SA10.011.01.2016
CRH (Slovensko) a.s.
Made in Slovakia

## Slide 40
Antifire System SA10.011.01.2016
CRH (Slovensko) a.s.
Made in Slovakia

## Slide 41
Antifire System SA10.011.01.2016
Made in Slovakia

## Slide 42
Antifire System SA10.011.01.2016

## Slide 43
Antifire System SA10.004.01.2016
Hyundai DYMOS Slovakia s.r.o.

## Slide 44
Antifire System SA10.004.01.2016
Hyundai DYMOS Slovakia s.r.o.
Made in Slovakia

## Slide 45
Antifire System SA10.004.01.2016
Hyundai DYMOS Slovakia s.r.o.
Made in Slovakia

## Slide 46
Antifire System SA10.004.01.2016
Hyundai DYMOS Slovakia s.r.o.
Made in Slovakia

## Slide 47
MPH – 9
A heat generator

## Slide 48
MPH – 9
A heat generator

## Slide 49
Bombardier Transportation Czech Republic, a.s.
Antifire System SA10.003.02.2016

## Slide 50
MPH-4
MPH-9
Bombardier Transportation Czech Republic, a.s.
Made in Slovakia
Antifire System SA10.003.02.2016

## Slide 51
Hyundai DYMOS Czech s.r.o.
Antifire System SA10.008.01.2016

## Slide 52
Hyundai DYMOS Czech s.r.o.
Antifire System SA10.008.01.2016

## Slide 53
Hyundai DYMOS Czech s.r.o.
Antifire System SA10.008.01.2016

## Slide 54
Hyundai DYMOS Czech s.r.o.
Antifire System SA10.008.01.2016

## Slide 55
MPH – 9
MPH – 6
Stock Judetul Mures, Romania
The production line in Judetul Mures, Romania

## Slide 56
MPH – 6

## Slide 57
MPH – 6
MPH – 4
Garage in Nitra, Slovakia
The generation container in Czech Republic

## Slide 58
MPH – 6
Warehouse in Pardubice, Czech Republic
MPH - 24

## Slide 59
TPS – S – 01

## Slide 61
MPH – 4
Marec, 2016, Slovnaft

## Slide 62
MPH – 5M

## Slide 63
Synthesia, a.s., Pardubice, Czech Republic
Antifire System SA10.007.02.2016

## Slide 64
MPH – 10 st
MPH – 2
Cable channels in Pardubice, Synthesia a.s.
Dĺžka, m | 1120
MPH-10st, pieces | 68
MPH-9, pieces | 15
MPH-6, pieces | 20
MPH-5, pieces | 22
TPS-01-72, pieces | 129

## Slide 65
Antifire System SA10.007.02.2016
Cable channel

## Slide 66
Antifire System SA10.007.02.2016
Cable channel

## Slide 67
Antifire System SA10.007.02.2016
Cable channel

## Slide 68
Antifire System SA10.007.02.2016
Cable channel

## Slide 69
MPH – 4
Wind electricity production station , Steinberg & CO

## Slide 70
Škoda AUTO, a.s., Mladá Boleslav, Czech Republic
Fire System SA10.012.02.2016

## Slide 71
Fire System SA10.012.02.2016
Škoda AUTO, a.s., Mladá Boleslav, Czech Republic

## Slide 72
Aupark Bratislava
Fire System SA10.014.01.2016

## Slide 73
Aupark Bratislava
Fire System SA10.014.01.2016

## Slide 74
Aupark Bratislava
Fire System SA10.014.01.2016

## Slide 75
Aupark Bratislava
Fire System SA10.014.01.2016

## Slide 76
OLO as s.r.o. Bratislava
Fire System SA10.015.04.2016

## Slide 77
OLO as s.r.o. Bratislava
Fire System SA10.015.04.2016 Gas station

## Slide 78
OLO as s.r.o. Bratislava
Fire System SA10.015.04.2016 Gas station

## Slide 79
OLO as s.r.o. Bratislava
Fire System SA10.015.04.2016 Gas station

## Slide 80
OLO as s.r.o. Bratislava
Fire System SA10.015.04.2016 Turbogenerator

## Slide 81
OLO as s.r.o. Bratislava
Fire System SA10.015.04.2016 Turbogenerator

## Slide 82
OLO as s.r.o. Bratislava
Fire System SA10.015.04.2016 Turbogenerator

## Slide 83
Sapfir s.r.o.
Záhradná 19, 90024 Veľký Biel, Slovak Republic
Phone in Slovakia: +421245916247, +421907748884 Phone in Germany: +491755737565
info@sapfir-sro.eu
www.sapfir-sro.eu
Partner in Latvia: FN SERVISS
www.fnserviss.lv
Tel: